## Slide 1: Kick Over Tools
MALKYZIDEK YEHU JERRY

## Slide 2: Contents :
Type kick over tools
Kick over tools(OK6)
Ok6 parts
How to pinning OK6
OK6 sequence
Running tool
Pulling tools

## Slide 3: Type off kick over tools

## Slide 4: Kick over tool(0K6)
Initially a Camco design
For 1” valves
OK series : OK 6
Built in catcher
Re-pin trigger each run

## Slide 7
Important
Shear pins must be either free cutting brass(ASTM specification B16 half-hard)or aluminum alloy 5052 with H38 temper. If the shear pin made of anything harder, the kick over tool could be damaged or the pins might not shear.(pin size 3/16-1/4)

## Slide 8: OK sequence 1
Valve pinned to running tool
Running tool attached to Kickover Tool
Kickover tool pinned and straight

## Slide 9: OK sequence 2
RIH
Pass thru SPM’s
Pass thru target SPM

## Slide 10: OK sequence 3
Trigger orients in sleeve
Turns tool to align over pocket

## Slide 12: Orienting sleeve

## Slide 13: OK sequence 4
Trigger moves up orienting slot
At top – force is applied
Tools “kicks over”

## Slide 14: OK sequence 5
Valve – or pulling tool (shown) aligned over pocket

## Slide 15: OK sequence 6
Tools lowered onto valve (or into pocket)
Tap down to position valve
Or Jar up to pull valve

## Slide 17: Gas lift running tool
GA-2
- Bottom latch
JK-1
- Top latch

## Slide 19: Pulling tools