## Slide 1
SAFETY TALK : LADDER SAFETY
NAME : BENNYLOVE BENJAMIN
DESIGNATION : SLICKLINE ASSISTANT
JOIN DATE : 27 SEPTEMBER 2021

## Slide 2: LADDER SAFETY
PURPOSE : LADDER present unique opportunities for unsafe act and unsafe condition.

## Slide 3: LADDER HAZARDS
Hazard include:
Ladder with missing or broken parts.
Using a ladder with too low a weight rating.
Using a ladder that is too short for purpose.
Using metal ladder near energized electrical equipment.
Using ladders as a working platform
Objects falling from ladders.

## Slide 4: LADDER INSPECTION
Inspect ladders before each use:
All rungs and steps are free of oil, grease, dirt.
All fiitings are tight.
Spreaders or other locking devices are in place.
Non-skid safety feet are in place.
No structural defects, all support braces intact.
DO NOT use broken ladders. Have broken ladders tagged “Do Not Use” and removed from service.

## Slide 5: LADDER SETUP
PROCEDURE TO PREVENT LADDER INCIDENT:
Place ladder on a clean slip free level surface.
Extend the ladder 3-4 feet above the top of support if used to access roof or other elevated surface.
Anchor or secure the top of the ladder when the 3-4 foot extension is not possible.
Placed the ladder base ¼ the height of the ladder from the wall when using a straight ladder.

## Slide 6: LADDER SETUP (CONTINUED)
Never allow more than one person on a ladder.
Use tools belts or hand lines to carry object .
Do not lean out from the ladder in any direction.
If you have fear of heights – don’t climb a ladder.
Do not allow others to work under a ladder in use.

## Slide 7: LADDER MAINTENANCE
Keep ladders clean.
Never replace broken parts unless provided by the original manufacturer.
Do not attempt to repair broken side rails.
Keep all threaded fasteners properly adjusted.

## Slide 8: FIVE RULES OF LADDER SAFETY
Select right ladder for the job.
Inspect ladder before use it.
Setup ladder with care.
Climb and descend ladder cautiously.
Use safe Practices when working on a ladder.
Face ladder and hold on with both hands.
Carry tools on belt or raise and lower with hand line.
Check shoes and rungs for slippery surfaces.
Always hold on with one hand and never reach too far to either side or rear to maintain balance.
Never climb higher than second step from top on a stepladder or third from the top on a straight ladder.
Never attempt to move, shift or extend ladder while in use.

## Slide 9
THANK YOU GUYS FOR LISTENING! TOGETHER WE LEARN, TOGETHER WE WORK AS A TEAM! DB THE BEST!